## Slide 1: Instructor Notes
To the instructor:
This slide set has been prepared with both the highlights from the student text as well as notes from the text. The students will not be able to see the notes unless you provide them with the slide set. You can choose whether to provide that option.
The notes are best seen by directing the main presentation to the LCD projector and keeping the Notes view open on the instructor’s PC. You will find that stopping the presentation to do some kind of activity at least once every 20 minutes is critical to keeping PowerPoint from become tedious. Since different people have different presenting styles, it would be impossible to provide a clear timing structure. You should allow ample time for each slide, including stopping for activities.
In case you have not done this before, the instructor notes are found by pointing at Slide Show on the Menu Bar. Click on the Set Up Slide Show option and select Multiple Monitors  Show Presenter View.
Note: Presenter View also has a blackout button. Don’t be afraid to use it to interrupt the tedium of staring at an LCD presentation when doing activities.

## Slide 2: Advanced AndroidTM Application Development, Fourth Edition Chapter 16 Using Android’s Optional Hardware APIs

## Slide 3: Chapter 16 Overview
Working with Bluetooth
Working with USB
Working with Android Beam
Working with Wi-Fi

## Slide 4: Working with Bluetooth
Bluetooth APIs have been available since API Level 5, though not all Android devices have Bluetooth hardware.
However, this is a popular consumer feature that Android developers can use to their advantage.
Android 4.3 (API Level 18) introduced support for Bluetooth Low Energy (BLE), which uses a lot less power than Classic Bluetooth and allows your application to connect to Bluetooth Low Energy peripheral devices.

## Slide 5: Working with Bluetooth
When Bluetooth hardware is present, Android applications can
  Scan for and discover Bluetooth devices and interact with the Bluetooth adapter
  Establish RFCOMM connections and transfer data to and from devices via data streams
  Maintain point-to-point and multipoint connections with Bluetooth devices and manage multiple connections
  Connect to and communicate with Bluetooth Low Energy peripheral devices

## Slide 6: Working with Bluetooth
Both Bluetooth APIs are part of the android.bluetooth package.
As you might expect, the application must have permission to use the Bluetooth services.
  The android.permission.BLUETOOTH permission is required to connect to Bluetooth devices.
  Similarly, Android applications must have the android.permission.BLUETOOTH_ADMIN permission to administer Bluetooth hardware and related services, which includes managing tasks, enabling or disabling the hardware, and performing discovery scans.

## Slide 7: Working with Bluetooth
For Classic Bluetooth, the APIs are divided into several useful classes, including the following:
  The BluetoothAdapter class represents the Bluetooth radio hardware on the local device.
  The BluetoothDevice class represents a remote Bluetooth device.
  The BluetoothServerSocket class is used to open a socket to listen for incoming connections and provides a BluetoothSocket object when a connection is made.
  The BluetoothSocket class is used by the client to establish a connection to a remote device. After the device is connected, the BluetoothSocket object is used by both sides to handle the connection and retrieve the input and output streams.

## Slide 8: Working with Bluetooth
For Bluetooth LE, the APIs differ and are divided into their own classes:
  The BluetoothManager class is used to acquire the BluetoothAdapter using the getSystemService() method passing in the Context.BLUETOOTH_SERVICE value.
  The BluetoothAdapter class requires implementing the LeScanCallback interface to access the BluetoothDevice object using the onLeScan() method call.
  The BluetoothDevice class requires calling the connectGatt() method to connect to a peripheral Bluetooth LE device.

## Slide 9: Checking for the Existence of Bluetooth Hardware
    BluetoothAdapter btAdapter =
    BluetoothAdapter.getDefaultAdapter();
    if (btAdapter == null) {
    Log.d(DEBUG_TAG, "No bluetooth available.");
    // ...
    } else {
    // bt available
    }
Notes: The first thing to do when trying to enable Bluetooth functionality in your application is to establish whether or not the device has a Bluetooth radio. You can do this by calling and checking the return value of the BluetoothAdapter class’s static method called getDefaultAdapter().

## Slide 10: Enabling Bluetooth
After you have determined that the device has a Bluetooth radio, you need to check to see whether it is enabled using the BluetoothAdapter class method called isEnabled().
If the Bluetooth adapter is enabled, you can proceed.
Otherwise, you need to request that it be turned on.

## Slide 11: Enabling Bluetooth
If you need to request that Bluetooth be turned on, this can be done in several ways:
  Fire off the BluetoothAdapter.ACTION_REQUEST_ENABLE intent using the startActivityForResult() method. This launches an Activity that enables the user to choose to turn on the Bluetooth adapter. If the result is RESULT_OK, Bluetooth has been enabled; otherwise, the user canceled the Bluetooth-enabling process.
  Call the BluetoothAdapter enable() method. This method should be used only by applications that need to explicitly enable the Bluetooth radio. It requires the BLUETOOTH_ADMIN permission. In addition, it should be performed only as the result of a direct request from the user, such as through a button, menu item, or query dialog.
  The process of making an Android device discoverable also automatically enables Bluetooth. This can be achieved by firing off the BluetoothAdapter.ACTION_REQUEST_DISCOVERABLE intent using the startActivityForResult() method. This launches an Activity that presents the user with a choice to make the ­device discoverable for a set amount of time.

## Slide 12: Querying for Paired Devices
  Set<BluetoothDevice> pairedBtDevices = btAdapt.getBondedDevices();
Notes: You can use the BluetoothAdapter to query for available Bluetooth devices to connect to. The getBondedDevices() method returns a set of BluetoothDevice objects that represent the devices paired to the Bluetooth adapter.

## Slide 13: Discovering Devices
New Bluetooth devices must be discovered and paired to the adapter before use.
You can use the BluetoothAdapter to start and stop the discovery process for available Bluetooth devices to connect to.
The startDiscovery() method starts the discovery process asynchronously.
This method requires the android.permission.BLUETOOTH_ADMIN permission.

## Slide 14: Discovering Devices
After you have initiated the discovery process, your application needs to register to receive broadcasts for the following Intent actions:
  ACTION_DISCOVERY_STARTED: Occurs when the discovery process initiates
  ACTION_FOUND: Occurs each time a remote Bluetooth device is found
  ACTION_DISCOVERY_FINISHED: Occurs when the discovery process completes
Notes: The discovery process is resource- and time-intensive. You can use the isDiscovering() method to test whether the discovery process is currently under way. The cancelDiscovery() method can be used to stop the discovery process. This method should also be used any time a connection is about to be established with a remote Bluetooth device.

## Slide 15: Establishing Connections between Devices
The general idea behind connecting two devices via Bluetooth is for one device to find the other device by whatever means necessary, depending upon whether it is a previously paired device or is found through discovery.
After it’s found, the device calls the connect() method. Both devices then have a valid BluetoothSocket object that can be used to retrieve the InputStream and OutputStream objects for initiating data communications between the two devices.
Notes: Now, that’s where the theory ends and reality sets in. If it’s the same application running on both devices, both devices should find a remote device and both should be discoverable so they can also be found. Also, they should open a listening socket via the BluetoothServerSocket object so they can receive incoming connection requests and be able to connect to the other device. Add to that the fact that both the calls to the accept() method of the BluetoothServerSocket class and to the connect() method of the BluetoothSocket class are blocking synchronous calls, and you can quickly see that you need to use some threads here. Discovery also uses a fair amount of the Bluetooth hardware resources, so you need to cancel and then later restart this process as appropriate. Performing discovery during a connection or even while attempting a connection will likely lead to negative device performance.

## Slide 16: Establishing Connections between Devices
Notes: This figure shows a reasonable layout for a Bluetooth implementation and the threads used in the SimpleWireless project.

## Slide 17: Working with USB
The Android platform supports a variety of flexible USB-related features.
Android devices can act as both USB peripherals (client devices) and USB hosts, depending on the circumstances.
This expands the opportunities available for developers to extend the reach of their applications to a variety of situations.
Android devices can act as remote controllers or be controlled by accessories.
You can even use the Android Open Accessory Development Kit (ADK) to create new Android hardware accessories.

## Slide 18: Working with USB Accessories
In accessory mode, the approved accessory acts as a controller, providing power to the Android device.
  Data can be transferred in both directions.
The USB accessory APIs can be found under the android.hardware.usb package.
  They were introduced in Android 3.1 (API Level 12).
Your application can interface with USB accessories by accessing the USB system service using the Context.getSystemService() method.
You can use the UsbManager class (android.hardware.usb.UsbManager) to discover and communicate with any USB accessories connected to the device.

## Slide 19: Working with USB Accessories
The UsbManager class has a getAccessoryList() method, which lists all connected USB accessories available to the application.
You can also set up a broadcast receiver to be notified when specific USB accessories are connected.
Each USB accessory is represented as a UsbAccessory (android.hardware.usb.UsbAccessory) object.
In order to connect to a USB accessory, you need to request permission from the user.
When your application has received permission to communicate with the accessory, it can open a connection to the accessory and communicate using streams.
  This communication should be handled off the main UI thread.
When it is complete, you can terminate your application’s connection to the accessory.

## Slide 20: Working with USB Accessories
Applications that rely on USB accessories have numerous Android manifest file configuration details to consider.
At minimum, applications should declare a <uses-feature> tag with the android.hardware.usb.accessory feature and set their minimum SDK to API Level 12 or higher.

## Slide 21: Working as a USB Host
In host mode, the Android device acts as a controller, providing power to the connected USB device.
  Data can be transferred in both directions.
The USB hosts APIs can be found under the android.hardware.usb package.
  It was introduced in Android 3.1 (API Level 12).
Your application can interface with USB devices by accessing the USB system service using the Context.getSystemService() method.
You can use the UsbManager class (android.hardware.usb.UsbManager) to discover and communicate with any USB devices available.
You can also set up a broadcast receiver to be notified when specific USB devices are connected.

## Slide 22: Working as a USB Host
The UsbManager class has a getDeviceList() method that lists all connected USB devices available to the application.
Each USB device is represented as a UsbDevice (android.hardware.usb.UsbDevice) object.
To connect to a USB device, you need to request permission from the user.
After your application has received permission to communicate with the device, it can open a connection to the device; this communication should be handled off the main UI thread.
The Android SDK includes a number of classes for facilitating communication, including the UsbInterface, UsbEndpoint, UsbDeviceConnection, and UsbRequest classes (see the android.hardware.usb package for class details).
After it is complete, you can terminate your application’s connection to the device.
Applications that act as USB hosts have numerous Android manifest file configuration details to consider.
At minimum, applications should declare a <uses-feature> tag with the android.hardware.usb.host feature and set their minimum SDK to API Level 12 or higher.

## Slide 23: Working with Android Beam
NFC isn’t a new technology, but lately it’s been gaining traction with Google’s introduction of NFC in Android handsets starting with API Level 9. Previously, you’d be lucky to find it in anything but Nokia devices.
The NFC technology from Google is called Android Beam, which is an easy-to-market name for NDEF (NFC Data Exchange Format) Push over NFC and is available in API Level 14 and later.

## Slide 24: Enabling Android Beam Sending
Sending is enabled by default and triggers automatically.
When another NFC device is in range, the system shrinks the current screen of the foreground application and displays a message, “Touch to beam.”
If your application has no data to send, nothing happens.

## Slide 25: Enabling Android Beam Sending
Notes: An app (Google Play Music) in “Touch to beam” mode when near another NFC device.

## Slide 26: Enabling Android Beam Sending
  mNfcAdapter.setNdefPushMessageCallback(new CreateNdefMessageCallback() {
  @Override
  public NdefMessage createNdefMessage(NfcEvent event) {
  Time time = new Time();
  time.setToNow();
  String message = messageToBeam.getText().toString();
  String text = (message + " \n[Sent @ "
  + time.format("%H:%M:%S") + "]");
  byte[] mime = MIMETYPE.getBytes(Charset.forName("US-ASCII"));
  NdefRecord mimeMessage = new NdefRecord(
  NdefRecord.TNF_MIME_MEDIA, mime,
  new byte[0], text.getBytes());
  NdefMessage msg = new NdefMessage(
  new NdefRecord[] { mimeMessage,NdefRecord.
  createApplicationRecord("com.advancedandroidbook.simplewireless") });
  return msg;
  }
  }, this);
Notes: What you want to know about is sending data with this tap. That’s easy; just get an instance of the NfcAdapter class and call the setNdefPushMessageCallback() method with a valid CreateNdefMessageCallback instance.
The implementation of the createNdefMessage() method gets a String from an EditText control (messageToBeam), adds the time to it, and encapsulates it inside an NdefRecord object that is, itself, encapsulated in an NdefMessage. This message is returned and the system pushes it to the other device. You can register to be informed when the message has been successfully sent using the setOnNdefPushCompleteCallback() method of the NfcAdapter.

## Slide 27: Receiving Android Beam Messages
<intent-filter>
<action android:name="android.nfc.action.NDEF_DISCOVERED" />
<category android:name="android.intent.category.DEFAULT" />
<data android:mimeType=
"application/com.advancedandroidbook.simplewireless" />
</intent-filter>
Notes: Receiving messages is even more straightforward. Your Activity needs a new intent filter. Conveniently, NDEF messages come in as normal Intent objects.

## Slide 28: Receiving Android Beam Messages
    @Override
    public void onResume() {
    super.onResume();
    // Did we receive an NDEF message?
    Intent intent = getIntent();
    if (NfcAdapter.ACTION_NDEF_DISCOVERED.equals(intent.getAction())) {
    try {
    Parcelable[] rawMsgs = intent
    .getParcelableArrayExtra(NfcAdapter.EXTRA_NDEF_MESSAGES);
    // we created the message, so we know the format
    NdefMessage msg = (NdefMessage) rawMsgs[0];
    NdefRecord[] records = msg.getRecords();
    byte[] firstPayload = records[0].getPayload();
    String message = new String(firstPayload);
    mStatusText.setText(message);
    } catch (Exception e) {
    Log.e(DEBUG_TAG, "Error retrieving beam message.", e);
    }
    }
    }
Notes: Then you need to check the Intent content to see whether it has an NDEF message. If so, extract the data you’re looking for. This is just reversing the NdefMessage and NdefRecord creation from previously.

## Slide 29: Receiving Android Beam Messages
Notes: Sending the message (left) and receiving it (right).
Incorporating Android Beam into your applications can be that easy.

## Slide 30: Configuring the Manifest File for Android Beam
    <uses-sdk
    android:minSdkVersion="14"
    android:targetSdkVersion="19" />
    <uses-permission
    android:name="android.permission.NFC" />
    <uses-feature
    android:name="android.hardware.nfc"
    android:required="true" />
Notes: Android Beam requires API Level 14. Using NFC requires the android.permission.NFC permission to be added to the application’s Android manifest file. Additionally, android.hardware.nfc should be added as a <uses-feature> value to help app stores filter your application correctly to devices that have NFC hardware.

## Slide 31: Android Beam over Bluetooth
Android 4.1 (API Level 16) introduced a new feature for handing off NFC data transfers.
NFC was not designed to transfer large amounts of data, nor does NFC transfer data quickly.
One way to get around this limitation is to initiate the wireless connection using NFC with the device you want transfer data to, and then hand off the actual data transfer to a faster transfer method such as Bluetooth.
To make use of this new feature, simply implement the NfcAdapter.CreateBeamUrisCallback interface or use the setBeamPushUris() method defining the Uri objects for transferring.
The connection over Bluetooth is then handled automatically without your needing to implement any Bluetooth features yourself.

## Slide 32: Introducing Host Card Emulation
Android 4.4 (API Level 19) brought new NFC functionality to the Android platform, known as host card emulation.
Host card emulation allows an Android application to emulate an NFC card, rather than requiring the secure element of the device to act as the NFC card.
This feature opens up many possibilities for new NFC card applications that may not have been possible before, as data is transported securely from the NFC controller to your application and back.

## Slide 33: Working with Wi-Fi
Developers can also integrate Wi-Fi features into their applications in two main ways.
They can work with the Wi-Fi system service to find and connect to various Wi-Fi networks.
Newer versions of the Android SDK also support Wi-Fi Direct, which helps facilitate connections.

## Slide 34: Introducing Wi-Fi Direct
Wi-Fi Direct is a relatively new standard that attempts to solve the problems and difficulties with ad hoc Wi-Fi—namely, configuration and connection management—and it first appeared in the Android SDK in Android 4.0 (API Level 14).
In doing so, a host Wi-Fi Direct device basically becomes an access point, and a variation of the Protected Setup protocol is used to connect the two devices.
With longer range, faster data communications, and simpler networking than Bluetooth, some think Wi-Fi Direct will ultimately replace Bluetooth for certain kinds of connections.

## Slide 35: Introducing Wi-Fi Direct
Using Wi-Fi Direct on Android is fairly straightforward.
  Start by checking out the peer-to-peer Wi-Fi package android.net.wifi.p2p.
Using the WifiP2pManager class (android.net.wifi.p2p.WifiP2pManager), you configure several callback classes that are used to asynchronously get the status of requests you make.
You can also configure a broadcast receiver to handle various notifications as the state of Wi-Fi Direct changes, both in response to your requests and in changing availability of devices.

## Slide 36: Introducing Wi-Fi Direct
In terms of permissions, there is no distinction between regular Wi-Fi and Internet access and Wi-Fi Direct and peer-to-peer networking access.
You need permissions for INTERNET, ACCESS_WIFI_STATE, ACCESS_NETWORK_STATE, CHANGE_WIFI_STATE, and CHANGE_NETWORK_STATE.
Wi-Fi Direct requires API Level 14.

## Slide 37: Monitoring Wi-Fi State
The Wi-Fi sensor can read network status and determine nearby wireless access points.
The Android SDK provides a set of APIs for retrieving information about the Wi-Fi networks available to the device and Wi-Fi network connection details.
This information can be used for tracking signal strength, finding access points of interest, or performing actions when connected to specific access points.

## Slide 38: Monitoring Wi-Fi State
<uses-permission
android:name="android.permission.CHANGE_WIFI_STATE" />
<uses-permission
android:name="android.permission.ACCESS_WIFI_STATE" />
Notes: These samples require two explicit permissions in the AndroidManifest.xml file. The CHANGE_WIFI_STATE permission is needed when an application is accessing information about Wi-Fi networks that can turn on the Wi-Fi radio, thus changing its state. The ACCESS_WIFI_STATE permission is also needed to request any information from the Wi-Fi device. You can add these to the AndroidManifest.xml file as shown here.

## Slide 39: Monitoring Wi-Fi State
WifiManager wifi =
(WifiManager) getSystemService(Context.WIFI_SERVICE);
Notes: The next thing the application needs is an instance of the WifiManager object. It is a system service, so the getSystemService() method works.

## Slide 40: Monitoring Wi-Fi State
Now that the WifiManager object is available, the application can do something interesting or useful with it.
First, the application performs a Wi-Fi scan to see what access points are available in the local area.
You need to complete a few steps to perform a scan:
  Start the scan with the startScan() method of the WifiManager object.
  Register a BroadcastReceiver for the SCAN_RESULTS_AVAILABLE intent.
  Call getScanResults() to get a list of ScanResult objects.
  Iterate over the results and do something with them.

## Slide 41: Monitoring Wi-Fi State
  wifi.startScan();
  registerReceiver(rcvWifiScan,
  new IntentFilter(WifiManager.SCAN_RESULTS_AVAILABLE_ACTION));
Notes: You can perform the first two steps with the code shown here.

## Slide 42: Monitoring Wi-Fi State
      rcvWifiScan = new BroadcastReceiver() {
      public void onReceive(Context context, Intent intent) {
      List<ScanResult> resultList = wifi.getScanResults();
      int foundCount = resultList.size();
      Toast.makeText(WiFi.this,
      "Scan done, " + foundCount + " found",
      Toast.LENGTH_SHORT).show();
      ListIterator<ScanResult> results = resultList.listIterator();
      String fullInfo = "Scan Results : \n";
      while (results.hasNext()) {
      ScanResult info = results.next();
      String wifiInfo = "Name: " + info.SSID +
      "; capabilities = " + info.capabilities +
      "; sig str = " + info.level + "dBm";
      Log.v("WiFi", wifiInfo);
      fullInfo += wifiInfo + "\n";
      }
      status.setText(fullInfo);
      }
      };
Notes: The sample BroadcastReceiver object, shown here, performs the last two steps. It is called regularly until the stopScan() method is called on the WifiManager object.
The ScanResult object contains a few more fields than are demonstrated here. However, the Service Set Identifier (SSID), or name, property is probably the most recognizable to users. The capabilities property lists such things as what security model can be used (such as WEP). The signal strength (level), as given, isn’t all that descriptive for most users.
However, the WifiManager object provides a couple of helper methods for dealing with signal levels. The first is calculateSignalLevel(), which effectively turns the number into a particular number of “bars” of strength. You can use the second, compareSignalLevel(), to compare the relative signal strengths of two results.

## Slide 43: Monitoring Wi-Fi State
    ListIterator<WifiConfiguration> configs =
    wifi.getConfiguredNetworks().listIterator();
    String allConfigs = "Configs: \n";
    while (configs.hasNext()) {
    WifiConfiguration config = configs.next();
    String configInfo = "Name: " + config.SSID +
    "; priority = " + config.priority;
    Log.v("WiFi", configInfo);
    allConfigs += configInfo + "\n";
    }
    status.setText(allConfigs);
Notes: You can use the WifiManager object to list known access points. These are typically access points that the user has configured or connected to in the past. This code demonstrates the use of the getConfiguredNetworks() method.
The returned WifiConfiguration object does not include all the fields that it could. For instance, it does not fill any network key fields. It does, however, fill in similar fields to those found in the ScanResults object. This can be used, for instance, to notify the users when they are in range of known Wi-Fi networks if their devices are set to not automatically connect.
You can use the WifiManager object to configure Wi-Fi networks, get the state of the Wi-Fi radio, and more. See the android.net.wifi package for more information.

## Slide 44: Chapter 16 Summary
We have learned how to work with Bluetooth.
We have learned how to work with USB.
We have learned how to work with Android Beam.
We have learned how to work with Wi-Fi.
Notes: Class homework assignment: Chapter Quiz Questions and Exercises listed at the end of the chapter.

## Slide 45: References and More Information
Android API Guides: “Bluetooth”:
  http://d.android.com/guide/topics/connectivity/bluetooth.html
Android API Guides: “Bluetooth Low Energy”:
  http://d.android.com/guide/topics/connectivity/bluetooth-le.html
Android SDK Reference documentation on the android.net.wifi.p2p package:
  http://d.android.com/reference/android/net/wifi/p2p/package-summary.html
Android API Guides: “Wi-Fi Peer-to-Peer”:
  http://d.android.com/guide/topics/connectivity/wifip2p.html
Wikipedia entry on Wi-Fi Direct:
  http://en.wikipedia.org/wiki/Wi-Fi_Direct

## Slide 46: References and More Information
Android Training: “Sharing Files with NFC”:
  http://d.android.com/training/beam-files/index.html
Android API Guides: “Near Field Communication”:
  http://d.android.com/guide/topics/connectivity/nfc/index.html
Android SDK Reference documentation on the android.nfc package:
  http://d.android.com/reference/android/nfc/package-summary.html
Android API Guides: “USB Host and Accessory”:
  http://d.android.com/guide/topics/connectivity/usb/index.html
Android Tools: “Android Open Accessory Development Kit”:
  http://d.android.com/tools/adk/index.html